## Slide 1: Solace Performance Testing Harness
Christian Holtfurth
07/12/2017

## Slide 2: The Problem
The customer wants to know what kind of performance a broker can achieve on given infrastructure (on-prem/cloud)!
Gathering a full set of performance metrics on a broker takes a lot of time:
  Lot of tests with varying message sizes and fan-out ratios as well as different message types
  Each test needs to be run for a min amount of time to make sure we are not spooling etc.
  Lot of virtual hardware sizes to choose from and run tests on
  Sdkperf needs to be run across several hosts spreading traffic across several topics

## Slide 3: The Problem

## Slide 4: The Solution: Automate the hell out of it!!!
Use a combination of:
  Timed sdkperf publisher and consumer scripts
  Ansible playbook with asynchronous actions and polling to spin up sdkperf instances across several performance testing hosts and collect results
  Some bash, grep, awk, sed script magic to collect and calculate results
  Wrapper scripts to make it re-usable

## Slide 5: Overview of test setup
Pubhost1
Subhost1
Pubhost2
Subhost2
Pubhost3
Subhost3
Pubhost4
Subhost4
Ansible
Controller
Host
Ansible host runs the main scripts and ansible playbook, which:
  Pushes the Sdkperf files and scripts to the publisher and subscriber hosts
  Starts the Sdkperf consumers and publishers in async jobs with a timer
  Collects the results from all hosts and calculates the overall message throughput
  Decides whether test is success or fail based on target throughput number

## Slide 6: The Framework
Ansible Controller Host
Subhost
Pubhost
specific-test-sets/mytestset.sh
Defines up to 7 test arrays to run
with unlimited no of tests.
Each test sets parameters like:
- Msg size
- Fanout
- Target msg rate
- No of test hosts to use
- Msg type
- Prefix for logs/results
runtestset.sh
- Parses and breaks test set into
Individual test
- Collects output and calculates whether test was success/fail based on achieved/targeted rate and allowed error margin (default 5%)
run-tests.sh
Wrapper script around ansible
playbook:
- Calls ansible playbook
- Collects results from all hosts
- Calculates overall sum
start-sdk.yaml
Ansible playbook
- Pushes sdkperf and scripts to pub/sub hosts
- Starts the sdk_consumers across all subhosts
with a timer in an async job
- Starts the sdk_publishers across all pubhosts
with a timer in an async job
(each host get a portion of the target msg
rate assigned = overall / no of hosts)
- Collects the output of all publisher and
consumers across all hosts
sdkconsumers.sh
- Starts number of requested sdkperf consumers and pins them to
cores (no of publishers * by fanout) in background
- Waits for timer to expire or Control-C, which is then caught to
gracefully kill the sdkperf jobs and allow for their output to be
written
- Collects the results for each sdkperf job and calculates sum
sdkpublisher.sh
- Starts number of requested sdkperf publishers and pins them to
cores in background (each with a portion of the host target msg
rate = host rate / no of publishers)
- Waits for timer to expire or Control-C, which is then caught to
gracefully kill the sdkperf jobs and allow for their output to be
written
- Collects the results for each sdkperf job and calculates sum

## Slide 7: sdkconsumers.sh & sdkpublishers.sh

## Slide 8: sdkconsumers.sh

## Slide 9: sdkpublisher.sh

## Slide 10: sdkconsumers.sh & sdkpublisher.sh

## Slide 11: start_sdk.yaml

## Slide 12: start_sdk.yaml
Just a bit of pre-test setup…
  Create directories
  Copy scripts over
  Make them executable

## Slide 13: start_sdk.yaml
Starting sdks…
  async with runlength
  poll: 0 = fire & forget
  poll: 10 = wait for it
  item.index <= p. hosts
  with_items: each host with different topic
  register: to collect
  output later

## Slide 14: start_sdk.yaml
Collecting it…
  Tries to collect the results of the async jobs every 10 s for a previously calculates no of time
  Ignore_errors: True Don’t worry, we’ll do our error handling in the wrapper scripts

## Slide 15: run-tests.sh
You have seen this before…
Just a wrapper around the ansible playbook for mainly:
  Running a single test
  Calculating overall throughput numbers
  And: Error handling!

## Slide 16: run-testset.sh
You have seen this before…
Just a wrapper around the ansible playbook for mainly:
  Running a single test
  Calculating overall throughput numbers
  And: Error handling!

## Slide 17: A specific test set script
And here you define the performance metrics you are trying to achieve…
  Msg size
  Fanout
  Rate
  Pub hosts
  Msg type

## Slide 18
read -p “Questions?" question
while [ ! -z “${question}”] ; do
answer ${question}
read -p “Next question?" question
done